Name PD1579 ;
PartNo GAL22V10D ;
Date 20.03.2025 ;
Revision 01 ;
Designer Oleksandr Kolodkin ;
Company ZTR ;
Assembly MPUS 210040/00/01 ;
Location D19 ;
Device g22v10 ;

/* *************** INPUT PINS *********************/
PIN 1 = CLK ; /* CPU Clock */
PIN 3 = ACKN ; /* */
PIN 4 = A13 ; /* */
PIN 5 = A14 ; /* */
PIN 6 = A15 ; /* */
PIN 7 = MODE0 ; /* */
PIN 23 = MODE1 ; /* */
PIN 8 = S0 ; /* */
PIN 9 = S1 ; /* */
PIN 10 = IOM ; /* */
PIN 11 = MWAIT0 ; /* */
PIN 16 = MWAIT1 ; /* */

/* *************** OUTPUT PINS *********************/
PIN 21 = !ROM0_CS ; /* ROM D21 */
PIN 20 = !ROM1_CS ; /* ROM D24 (not soldered) */
PIN 22 = !RAM0_CS ; /* RAM D26 */
PIN 18 = !RAM1_CS ; /* RAM D29 */
PIN 17 = !BSRE ; /* Multibus */
PIN 19 = !READY ; /* */
PIN 14 = STATE0 ; /* Internal state */
PIN 15 = STATE1 ; /* Internal state */

FIELD ADDR = [A15..0];
FIELD MODE = [MODE1..0];
FIELD STATE = [STATE1..0];
FIELD S = [S1..0];

/* CPU State */
$DEFINE HALT 0 /* Processor halted */
$DEFINE WRITE 1 /* Write data to memory */
$DEFINE READ 2 /* Read data from memory */
$DEFINE FETCH 3 /* Fetch opcode from memory */
READY.ar = 'b'0;
READY.sp = 'b'0;

SEQUENCE READY {
  PRESENT 0
    IF BSRE NEXT 1;
    DEFAULT NEXT 0;

  PRESENT 1
    IF !BSRE NEXT 0;
    DEFAULT NEXT 1;
}

STATE0.ar = 'b'0;
STATE0.sp = 'b'0;
STATE1.ar = 'b'0;
STATE1.sp = 'b'0;

SEQUENCE STATE {
  PRESENT 0
    IF !MODE0 & !MODE1 NEXT 1;
    IF MODE0 & !MODE1 NEXT 2;
    IF !MODE0 & MODE1 NEXT 3;
    DEFAULT NEXT 0;

  PRESENT 1
    IF MODE0 & MODE1 NEXT 0;
    DEFAULT NEXT 1;

  PRESENT 2
    IF MODE0 & MODE1 NEXT 0;
    DEFAULT NEXT 2;

  PRESENT 3
    IF MODE0 & MODE1 NEXT 0;
    DEFAULT NEXT 3;
}

CONDITION {
  IF (IOM:0 & STATE:0 & MODE:3 & ADDR:[0000..7FFF]) OUT ROM0_CS;
  IF (IOM:0 & STATE:0 & MODE:3 & ADDR:[8000..FFFF]) OUT RAM1_CS;

  IF (IOM:0 & STATE:1 & MODE:0 & ADDR:[0000..7FFF]) OUT ROM0_CS;
  IF (IOM:0 & STATE:1 & MODE:0 & ADDR:[8000..BFFF]) OUT ROM1_CS;
  IF (IOM:0 & STATE:1 & MODE:0 & ADDR:[C000..DFFF]) OUT RAM1_CS;
  IF (IOM:0 & STATE:1 & MODE:0 & ADDR:[E000..FFFF]) OUT BSRE;
  IF (IOM:0 & STATE:1 & MODE:1 & ADDR:[0000..3FFF]) OUT ROM0_CS;
  IF (IOM:0 & STATE:1 & MODE:1 & ADDR:[4000..FFFF]) OUT RAM1_CS;
  IF (IOM:0 & STATE:1 & MODE:2 & ADDR:[0000..3FFF]) OUT ROM0_CS;
  IF (IOM:0 & STATE:1 & MODE:2 & ADDR:[4000..7FFF]) OUT RAM1_CS;
  IF (IOM:0 & STATE:1 & MODE:2 & ADDR:[8000..FFFF]) OUT RAM0_CS;

  IF (IOM:0 & STATE:2 & MODE:0 & ADDR:[0000..1FFF]) OUT ROM0_CS;
  IF (IOM:0 & STATE:2 & MODE:0 & ADDR:[2000..5FFF]) OUT ROM1_CS;
  IF (IOM:0 & STATE:2 & MODE:0 & ADDR:[6000..7FFF]) OUT RAM1_CS;
  IF (IOM:0 & STATE:2 & MODE:0 & ADDR:[8000..FFFF]) OUT BSRE;
  IF (IOM:0 & STATE:2 & MODE:1 & ADDR:[0000..5FFF]) OUT ROM0_CS;
  IF (IOM:0 & STATE:2 & MODE:1 & ADDR:[6000..7FFF]) OUT RAM1_CS;
  IF (IOM:0 & STATE:2 & MODE:1 & ADDR:[8000..FFFF]) OUT BSRE;
  IF (IOM:0 & STATE:2 & MODE:2 & ADDR:[0000..1FFF]) OUT ROM0_CS;
  IF (IOM:0 & STATE:2 & MODE:2 & ADDR:[2000..7FFF]) OUT RAM1_CS;
  IF (IOM:0 & STATE:2 & MODE:2 & ADDR:[8000..FFFF]) OUT BSRE;

  IF (IOM:0 & STATE:3 & MODE:0 & ADDR:[0000..7FFF]) OUT RAM0_CS;
  IF (IOM:0 & STATE:3 & MODE:0 & ADDR:[8000..FFFF]) OUT BSRE;
  IF (IOM:0 & STATE:3 & MODE:1 & ADDR:[0000..7FFF]) OUT RAM0_CS;
  IF (IOM:0 & STATE:3 & MODE:1 & ADDR:[8000..DFFF]) OUT RAM1_CS;
  IF (IOM:0 & STATE:3 & MODE:1 & ADDR:[E000..FFFF]) OUT BSRE;
  IF (IOM:0 & STATE:3 & MODE:2 & ADDR:[0000..7FFF]) OUT RAM0_CS;
  IF (IOM:0 & STATE:3 & MODE:2 & ADDR:[8000..FFFF]) OUT RAM1_CS;
  IF (IOM:1 & S:[READ, WRITE] & ADDR:[4000..FFFF]) OUT BSRE;
}